## Slide 1: CSC 101 – Introduction to Computing
Lecture 08 (Morley Ch 7)

## Slide 2: What Is a Network?
Network
  A connected system of objects or people
Computer network
  A collection of computers and other hardware devices connected together so users can share hardware, software, and data, and electronically communicate
Networks range from small private networks to the Internet

## Slide 3: Networking Applications
The Internet
  Largest computer network in the world
Telephone Service
  POTS (Plain Old Telephone Service) Network
    One of the first networks
    Still used today to provide telephone service to landline phones
  Mobile Phones (wireless phones)
    Use a wireless network for communications

## Slide 4: Networking Applications
Cellular (cell) Phones
  Must be within range of cell tower to function
Dual-mode Phones
  Allow users to make telephone calls using more than one communications network
  Cellular/Wi-Fi dual-mode phones can switch seamlessly between the Wi-Fi network and a cellular network
Satellite Phones
  Communicate via satellite technology
  Most often used by individuals such as soldiers, journalists, wilderness guides, and researchers

## Slide 5: Networking Applications
Television and Radio Broadcasting
  Still used to deliver TV and radio content to the public
  Other networks involved with television content delivery are cable TV networks, satellite TV networks, and private closed-circuit television systems
Global Positioning System (GPS) Applications
  Uses satellites and a receiver to determine the exact geographic location of the receiver
  GPS receivers
    Commonly used by individuals to determine their geographic location

## Slide 6: Networking Applications
Videoconferencing, Collaborative Computing, and Telecommuting
  Videoconferencing
    Use of computers, video cameras, microphones, and networking technologies to conduct face-to-face meetings over a network
  Telepresence Videoconferencing
    A setup that more closely mimics a real-time meeting environment

## Slide 7: Networking Applications
Collaborative Computing (workgroup computing)
  Enables individuals to work together on documents and projects
Telecommuting
  Individuals work from a remote location (usually home) and communicate with their places of business and clients using networking technologies
  Allows for employee flexibility

## Slide 8: Networking Applications
Telemedicine
  Use of networking technology to provide medical information and services
  Remote monitoring and consultations
  Remote diagnosis
  Telesurgery
    Robot assisted surgery where doctor’s physical location is different from the patient’s and robot’s

## Slide 9: Network Characteristics
Wired vs. Wireless Networks
  Wired
    A network in which computers and other devices are
physically connected to the network with cables
    Found in schools, businesses, and government facilities
  Wireless
    A network in which computers and other devices are connected to the network without physical cables
    Data is typically sent via radio waves
    Found in homes, schools, and businesses

## Slide 10: Network Characteristics
Network Topologies: Indicate how the devices in the network are arranged
  Star Networks
    All networked devices connect to a central device/server
    If the central device fails, the network cannot work
  Bus Network
    Uses a central cable to which all network devices connect
  Mesh network
    Multiple connections among the devices on the network so that messages can take any of several possible paths

## Slide 11: Network Characteristics

## Slide 12: Network Characteristics
Network Architectures
  Client-Server Networks
    Client
      Computer or other device on the network that requests and utilizes network resources
    Server
      Computer dedicated to processing client requests

## Slide 13: Network Characteristics
Peer-to-Peer (P2P) Networks
  Central server is not used
  All computers on the network work at the same
functional level
  Users have direct access to the computers and devices attached to the network
  Less complicated and less expensive to implement than client-server networks

## Slide 14: Network Characteristics
Network Size and Coverage Area
  Personal Area Networks (PANs)
    Connect an individual’s personal devices
– Devices must be physically located close together
  Local Area Networks (LANs)
    Connect devices located in a small geographic area
  Metropolitan Area Networks (MANs)
    Cover a metropolitan area such as a city or county
  Wide Area Networks (WANs)
    Cover a large geographic area
    Two or more LANs connected together

## Slide 15: Network Characteristics
Intranets and Extranets
  Intranet
    Private network designed to be used by an
organizations’ employees; set up like the Internet
  Extranet
    Company network accessible by authorized outsiders
Virtual Private Networks (VPNs)
  Private, secure path over the Internet that provides authorized users a secure means of accessing a private network via the Internet

## Slide 16: Data Transmission Characteristics
Bandwidth
  The amount of data that can be transferred in a given period of time
  Measured in bits per second (bps), Kbps (thousands), Mbps (millions ), or Gbps (billions)
Analog vs. Digital Signals
  Data represented by two discrete states: 0s and 1s
  Conventional telephone systems use
analog signals
    Represent data with continuous waves

## Slide 17: Data Transmission Characteristics
Transmission Type and Timing
  Serial
    Data sent one bit at a time, one after another, along a single path
  Parallel
    Data sent at least one byte at time with each bit in the byte taking a different path

## Slide 18: Data Transmission Characteristics
Synchronous Transmission
  Blocks of data are transferred at regular, specified intervals
  Most data transmissions within a computer and over a
network are synchronous
Asynchronous Transmission
  Data is sent when ready without being synchronized
  Start bits and stop bits used to identify the bits that belong in each byte
Isochronous Transmission
  Data sent at the same time as other, related, data

## Slide 19: Data Transmission Characteristics

## Slide 20: Data Transmission Characteristics
Simplex Transmission
  Data travels in a single direction only
Half-Duplex Transmission
  Data travels in either direction but only one way at a time
Full-Duplex Transmission
  Data travels in both directions at the same time

## Slide 21: Data Transmission Characteristics
Delivery Method
  Circuit-Switching
    Dedicated path over a network is established between
sender and receiver; all data follows that path
  Packet-Switching
    Messages are separated into small units called packets and travel along the network separately; packets are reassembled once destination is reached
  Broadcasting
    Data is sent out to all other nodes on the network and retrieved only by the intended recipient; primarily used with LANs

## Slide 22: Data Transmission Characteristics

## Slide 23: Networking Media
Wired Networking Media
  Twisted-Pair Cable
    Pairs of insulated wires twisted together
    Used for telephone and network connections (LANs)
  Coaxial Cable
    Thick center wire surrounded by insulation
    Used for cable television delivery
  Fiber-Optic Cable
    Utilizes hundreds of thin transparent clear glass or plastic fibers over which lasers transmit data as light
    Used for high-speed communications

## Slide 24: Networking Media

## Slide 25: Networking Media
Wireless Networking Media
  Data is sent through the airwaves using radio signals
  The Electromagnetic and Wireless Spectrum
    Radio frequencies are assigned by the FCC and are measured in hertz (Hz)
    The electromagnetic spectrum is the range of common
electromagnetic radiation (energy)
    Different parts of the spectrum have different properties, which make certain frequencies more appropriate for certain applications

## Slide 26: Networking Media

## Slide 27: Networking Media
Frequencies assigned to an application usually consist of a range of frequencies to be used as needed
Most wireless networking applications use frequencies in the RF band at the low end of the spectrum—up to 300 GHz
  Often called the wireless spectrum
The 900 MHz, 2.4GHz, 5 GHz, and 5.8 GHz frequencies are within an unlicensed part of the spectrum and can be used by any product or individual
  Cordless landline phones, garage door openers, Wi-Fi, WiMAX, and Bluetooth

## Slide 28: Networking Media
Cellular Radio Transmissions
  Use cellular towers within honeycomb-shaped zones called cells
  Calls are transferred from cell tower to cell tower as the individual moves
  Cell tower forwards call to the MTSO
  MTSO routes call to the recipient’s phone
  Data sent via cell phones works in similar manner
  The speed of cellular radio transmissions depends on the type of cellular standard being used

## Slide 29: Networking Media

## Slide 30: Networking Media
Microwave and Satellite Transmissions
  Microwaves
    High-frequency radio signals that are sent and received
using microwave stations or satellites
    Signals are line of sight, so microwave stations are usually built on tall buildings, towers, mountaintops
  Microwave stations
    Earth-based stations that transmit signals directly to each other within a range of 30 miles
    Stations designed to communicate with satellites (television and internet services) are called satellite dishes